## Slide 1: The Memory Hierarchy : Memory Hierarchy - Cache
Instructors:
Pelin Angin and Erol Sahin

## Slide 2: Storage Trends
Metric 1980 1985 1990 1995 2000 2005 2010 2010:1980
$/MB 8,000 880 100 30 1 0.1 0.06 130,000
access (ns) 375 200 100 70 60 50 40 9
typical size (MB) 0.064 0.256 4 16 64 2,000 8,000 125,000
DRAM
SRAM
Metric 1980 1985 1990 1995 2000 2005 2010 2010:1980
$/MB 500 100 8 0.30 0.01 0.005 0.0003 1,600,000
access (ms) 87 75 28 10 8 4 3 29
typical size (MB) 1 10 160 1,000 20,000 160,000 1,500,000 1,500,000
Disk
Metric 1980 1985 1990 1995 2000 2005 2010 2010:1980
$/MB 19,200 2,900 320 256 100 75 60 320
access (ns) 300 150 35 15 3 2 1.5 200

## Slide 3: CPU Clock Rates
1980 1990 1995 2000 2003 2005 2010 2010:1980
CPU 8080 386 Pentium P-III P-4 Core 2 Core i7 ---
Clock
rate (MHz) 1 20 150 600 3300 2000 2500 2500
Cycle
time (ns) 1000 50 6 1.6 0.3 0.50 0.4 2500
Cores 1 1 1 1 1 2 4 4
Effective
cycle 1000 50 6 1.6 0.3 0.25 0.1 10,000
time (ns)
Inflection point in computer history
when designers hit the “Power Wall”

## Slide 4: The CPU-Memory Gap
The gap widens between DRAM, disk, and CPU speeds.
Chart: Year
| 1980.0 | 1985.0 | 1990.0 | 1995.0 | 2000.0 | 2003.0 | 2005.0 | 2010.0
Disk seek time | 87000000 | 75000000 | 28000000 | 10000000 | 8000000 | 8000000 | 8000000 | 8000000
Flash SSD access time | 75000
DRAM access time | 375 | 200 | 100 | 70 | 60 | 55 | 50 | 40
SRAM access time | 300 | 150 | 35 | 15 | 3 | 2.5 | 2 | 1.5
CPU cycle time | 1000 | 166 | 50 | 6 | 1.6 | 0.3 | 0.5 | 0.4
Effective CPU cycle time | 0.3 | 0.25 | 0.1
Disk
DRAM
CPU
SSD

## Slide 5: Locality to the Rescue!
The key to bridging this CPU-Memory gap is a fundamental property of computer programs known as locality

## Slide 6: Locality
Principle of Locality: Programs tend to use data and instructions with addresses near or equal to those they have used recently
Temporal locality:
  Recently referenced items are likely to be referenced again in the near future
Spatial locality:
  Items with nearby addresses tend to be referenced close together in time

## Slide 7: Locality Example
Data references
  Reference array elements in succession (stride-1 reference pattern).
  Reference variable sum each iteration.
Instruction references
  Reference instructions in sequence.
  Cycle through loop repeatedly.
sum = 0;
for (i = 0; i < n; i++)
sum += a[i];
return sum;
Spatial locality
Temporal locality
Spatial locality
Temporal locality

## Slide 8: Qualitative Estimates of Locality
Claim: Being able to look at code and get a qualitative sense of its locality is a key skill for a professional programmer.
Question: Does this function have good locality with respect to array a?
int sum_array_rows(int a[M][N])
{
int i, j, sum = 0;
for (i = 0; i < M; i++)
for (j = 0; j < N; j++)
sum += a[i][j];
return sum;
}

## Slide 9: Locality Example
Question: Does this function have good locality with respect to array a?
int sum_array_cols(int a[M][N])
{
int i, j, sum = 0;
for (j = 0; j < N; j++)
for (i = 0; i < M; i++)
sum += a[i][j];
return sum;
}

## Slide 10: Locality Example
Question: Can you permute the loops so that the function scans the 3-d array a with a stride-1 reference pattern (and thus has good spatial locality)?
int sum_array_3d(int a[M][N][N])
{
int i, j, k, sum = 0;
for (i = 0; i < M; i++)
for (j = 0; j < N; j++)
for (k = 0; k < N; k++)
sum += a[k][i][j];
return sum;
}

## Slide 11: Memory Hierarchies
Some fundamental and enduring properties of hardware and software:
  Fast storage technologies cost more per byte, have less capacity, and require more power (heat!).
  The gap between CPU and main memory speed is widening.
  Well-written programs tend to exhibit good locality.
These fundamental properties complement each other beautifully.
They suggest an approach for organizing memory and storage systems known as a memory hierarchy.

## Slide 12: An Example Memory Hierarchy
Registers
L1 cache
(SRAM)
Main memory
(DRAM)
Local secondary storage
(local disks)
Larger,
slower,
cheaper
per byte
Remote secondary storage
(tapes, distributed file systems, Web servers)
Local disks hold files retrieved from disks on remote network servers
Main memory holds disk blocks retrieved from local disks
L2 cache
(SRAM)
L1 cache holds cache lines retrieved from L2 cache
CPU registers hold words retrieved from L1 cache
L2 cache holds cache lines retrieved from main memory
L0:
L1:
L2:
L3:
L4:
L5:
Smaller,
faster,
costlier
per byte

## Slide 13: Caches
Cache: A smaller, faster storage device that acts as a staging area for a subset of the data in a larger, slower device.
Fundamental idea of a memory hierarchy:
  For each k, the faster, smaller device at level k serves as a cache for the larger, slower device at level k+1.
Why do memory hierarchies work?
  Because of locality, programs tend to access the data at level k more often than they access the data at level k+1.
  Thus, the storage at level k+1 can be slower, and thus larger and cheaper per bit.
Big Idea: The memory hierarchy creates a large pool of storage that costs as much as the cheap storage near the bottom, but that serves data to programs at the rate of the fast storage near the top.

## Slide 14: General Cache Concepts
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Larger, slower, cheaper memory
viewed as partitioned into “blocks”
Data is copied in block-sized transfer units
Smaller, faster, more expensive
memory caches a subset of
the blocks
4
4
4
10
10
10

## Slide 15: General Cache Concepts: Hit
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Data in block b is needed
Request: 14
14
Block b is in cache:
Hit!

## Slide 16: General Cache Concepts: Miss
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Data in block b is needed
Request: 12
Block b is not in cache:
Miss!
Block b is fetched from
memory
Request: 12
12
12
12
Block b is stored in cache
Placement policy: determines where b goes
Replacement policy: determines which block gets evicted (victim)

## Slide 17: General Caching Concepts: Types of Cache Misses
Cold (compulsory) miss
  Cold misses occur because the cache is empty.
Conflict miss
  Most caches limit blocks at level k+1 to a small subset (sometimes a singleton) of the block positions at level k.
    E.g. Block i at level k+1 must be placed in block (i mod 4) at level k.
  Conflict misses occur when the level k cache is large enough, but multiple data objects all map to the same level k block.
    E.g. Referencing blocks 0, 8, 0, 8, 0, 8, ... would miss every time.
Capacity miss
  Occurs when the set of active cache blocks (working set) is larger than the cache.

## Slide 18: Examples of Caching in the Hierarchy
Hardware
0
On-Chip TLB
Address translations
TLB
Web browser
10,000,000
Local disk
Web pages
Browser cache
Web cache
Network buffer cache
Buffer cache
Virtual Memory
L2 cache
L1 cache
Registers
Cache Type
Web pages
Parts of files
Parts of files
4-KB page
64-bytes block
64-bytes block
4-8 bytes words
What is Cached?
Web proxy server
1,000,000,000
Remote server disks
OS
100
Main memory
Hardware
1
On-Chip L1
Hardware
10
On/Off-Chip L2
AFS/NFS client
10,000,000
Local disk
Hardware + OS
100
Main memory
Compiler
0
CPU core
Managed By
Latency (cycles)
Where is it Cached?
Disk cache
Disk sectors
Disk controller
100,000
Disk firmware

## Slide 19: Summary
The speed gap between CPU, memory and mass storage continues to widen.
Well-written programs exhibit a property called locality.
Memory hierarchies based on caching close the gap by exploiting locality.

## Slide 20: Cache
Cache memory organization and operation
Performance impact of caches
  The memory mountain
  Rearranging loops to improve spatial locality
  Using blocking to improve temporal locality

## Slide 21: Cache Memories
Cache memories are small, fast SRAM-based memories managed automatically in hardware.
  Hold frequently accessed blocks of main memory
CPU looks first for data in caches (e.g., L1, L2, and L3), then in main memory.
Typical system structure:
Main
memory
I/O
bridge
Bus interface
ALU
Register file
CPU chip
System bus
Memory bus
Cache
memories

## Slide 22: General Cache Organization (S, E, B)
E = 2e lines per set
S = 2s sets
set
line
0
1
2
B-1
tag
v
B = 2b bytes per cache block (the data)
Cache size:
C = S x E x B data bytes
valid bit

## Slide 23: Cache Read
E = 2e lines per set
S = 2s sets
0
1
2
B-1
tag
v
valid bit
B = 2b bytes per cache block (the data)
t bits
s bits
b bits
Address of word:
tag
set
index
block
offset
data begins at this offset
Locate set
Check if any line in set has matching tag
Yes + line valid: hit
Locate data starting at offset

## Slide 24: Example: Direct Mapped Cache (E = 1)
S = 2s sets
Direct mapped: One line per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
find set

## Slide 25: Example: Direct Mapped Cache (E = 1)
Direct mapped: One line per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
match: assume yes = hit
valid? +
block offset
tag

## Slide 26: Example: Direct Mapped Cache (E = 1)
Direct mapped: One line per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
match: assume yes = hit
valid? +
int (4 Bytes) is here
block offset
No match: old line is evicted and replaced

## Slide 27: Direct-Mapped Cache Simulation
M=16 byte addresses, B=2 bytes/block,
S=4 sets, E=1 Blocks/set
Address trace (reads, one byte per read):
0 [00002],
1 [00012],
7 [01112],
8 [10002],
0 [00002]
x
t=1
s=2
b=1
xx
x
0
?
?
v
Tag
Block
miss
1
0
M[0-1]
hit
miss
1
0
M[6-7]
miss
1
1
M[8-9]
miss
1
0
M[0-1]
Set 0
Set 1
Set 2
Set 3

## Slide 28: A Higher Level Example
int sum_array_rows(double a[16][16])
{
int i, j;
double sum = 0;
for (i = 0; i < 16; i++)
for (j = 0; j < 16; j++)
sum += a[i][j];
return sum;
}
32 B = 4 doubles
assume: cold (empty) cache,
a[0][0] goes here
int sum_array_cols(double a[16][16])
{
int i, j;
double sum = 0;
for (j = 0; j < 16; j++)
for (i = 0; i < 16; i++)
sum += a[i][j];
return sum;
}
Ignore the variables sum, i, j

## Slide 29: E-way Set Associative Cache (Here: E = 2)
E = 2: Two lines per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of short int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
find set

## Slide 30: E-way Set Associative Cache (Here: E = 2)
E = 2: Two lines per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of short int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
compare both
valid? +
match: yes = hit
block offset
tag

## Slide 31: E-way Set Associative Cache (Here: E = 2)
E = 2: Two lines per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of short int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
compare both
valid? +
match: yes = hit
block offset
short int (2 Bytes) is here
No match:
One line in set is selected for eviction and replacement
Replacement policies: random, least recently used (LRU), …

## Slide 32: 2-Way Set Associative Cache Simulation
M=16 byte addresses, B=2 bytes/block,
S=2 sets, E=2 blocks/set
Address trace (reads, one byte per read):
0 [00002],
1 [00012],
7 [01112],
8 [10002],
0 [00002]
xx
t=2
s=1
b=1
x
x
0
?
?
v
Tag
Block
0
0
0
miss
1
00
M[0-1]
hit
miss
1
01
M[6-7]
miss
1
10
M[8-9]
hit
Set 0
Set 1

## Slide 33: A Higher Level Example
int sum_array_rows(double a[16][16])
{
int i, j;
double sum = 0;
for (i = 0; i < 16; i++)
for (j = 0; j < 16; j++)
sum += a[i][j];
return sum;
}
32 B = 4 doubles
assume: cold (empty) cache,
a[0][0] goes here
int sum_array_rows(double a[16][16])
{
int i, j;
double sum = 0;
for (j = 0; j < 16; j++)
for (i = 0; i < 16; i++)
sum += a[i][j];
return sum;
}
Ignore the variables sum, i, j

## Slide 34: What about writes?
Multiple copies of data exist:
  L1, L2, Main Memory, Disk
What to do on a write-hit?
  Write-through (write immediately to memory)
  Write-back (defer write to memory until replacement of line)
    Need a dirty bit (line different from memory or not)
What to do on a write-miss?
  Write-allocate (load into cache, update line in cache)
    Good if more writes to the location follow
  No-write-allocate (writes immediately to memory)
Typical
  Write-through + No-write-allocate
  Write-back + Write-allocate

## Slide 35: Intel Core i7 Cache Hierarchy
Regs
L1
d-cache
L1
i-cache
L2 unified cache
Core 0
Regs
L1
d-cache
L1
i-cache
L2 unified cache
Core 3
…
L3 unified cache
(shared by all cores)
Main memory
Processor package
L1 i-cache and d-cache:
  32 KB, 8-way,
  Access: 4 cycles
L2 unified cache:
  256 KB, 8-way,
  Access: 11 cycles
L3 unified cache:
  8 MB, 16-way,
  Access: 30-40 cycles
Block size: 64 bytes for all caches.

## Slide 36: Cache Performance Metrics
Miss Rate
  Fraction of memory references not found in cache (misses / accesses) = 1 – hit rate
  Typical numbers (in percentages):
    3-10% for L1
    can be quite small (e.g., < 1%) for L2, depending on size, etc.
Hit Time
  Time to deliver a line in the cache to the processor
    includes time to determine whether the line is in the cache
  Typical numbers:
    1-2 clock cycle for L1
    5-20 clock cycles for L2
Miss Penalty
  Additional time required because of a miss
    typically 50-200 cycles for main memory (Trend: increasing!)

## Slide 37: Lets think about those numbers
Huge difference between a hit and a miss
  Could be 100x, if just L1 and main memory
Would you believe 99% hits is twice as good as 97%?
  Consider: cache hit time of 1 cycle miss penalty of 100 cycles
  Average access time:
  97% hits: 1 cycle + 0.03 * 100 cycles = 4 cycles
  99% hits: 1 cycle + 0.01 * 100 cycles = 2 cycles
This is why “miss rate” is used instead of “hit rate”

## Slide 38: Writing Cache Friendly Code
Make the common case go fast
  Focus on the inner loops of the core functions
Minimize the misses in the inner loops
  Repeated references to variables are good (temporal locality)
  Stride-1 reference patterns are good (spatial locality)
Key idea: Our qualitative notion of locality is quantified through our understanding of cache memories.

## Slide 39: Today
Cache organization and operation
Performance impact of caches
  The memory mountain
  Rearranging loops to improve spatial locality
  Using blocking to improve temporal locality

## Slide 40: The Memory Mountain
Read throughput (read bandwidth)
  Number of bytes read from memory per second (MB/s)
Memory mountain: Measured read throughput as a function of spatial and temporal locality.
  Compact way to characterize memory system performance.

## Slide 41: Memory Mountain Test Function
/* The test function */
void test(int elems, int stride) {
int i, result = 0;
volatile int sink;
for (i = 0; i < elems; i += stride)
result += data[i];
sink = result; /* So compiler doesn't optimize away the loop */
}
/* Run test(elems, stride) and return read throughput (MB/s) */
double run(int size, int stride, double Mhz)
{
double cycles;
int elems = size / sizeof(int);
test(elems, stride); /* warm up the cache */
cycles = fcyc2(test, elems, stride, 0); /* call test(elems,stride) */
return (size / stride) / (cycles / Mhz); /* convert cycles to MB/s */
}

## Slide 42: The Memory Mountain
Chart: Stride (x8 bytes)
| s1 | s2 | s3 | s4 | s5 | s6 | s7 | s8 | s9 | s10 | s11 | s12 | s13 | s14 | s15 | s16 | s32 | s64
64M | 4029.59 | 2752.75 | 2159.29 | 1710.75 | 1391.48 | 1176.29 | 1015.77 | 890.72 | 845.57 | 805.46 | 773.78 | 757.94 | 727.91 | 712.66 | 705.63 | 701.98 | 598.19 | 601.22
32M | 4029.36 | 2752.39 | 2160.62 | 1710.98 | 1391.5 | 1176.54 | 1016.71 | 891.8 | 846.98 | 807.22 | 775.18 | 760.41 | 730.74 | 714.98 | 709.26 | 708.88 | 608.99 | 607.39
16M | 4040.1 | 2788.42 | 2188.92 | 1742.97 | 1421.69 | 1201.31 | 1038.37 | 911.7 | 870.39 | 835.31 | 809.25 | 798.05 | 780.28 | 778.37 | 787.2 | 744.13 | 633.53 | 608.86
8M | 4374.01 | 3610.74 | 3002.03 | 2492.39 | 2131.04 | 1821.71 | 1564.14 | 1414.18 | 1404.78 | 1408.59 | 1423.67 | 1456.86 | 1499.61 | 1600.13 | 1667.47 | 1231.7 | 1078.97 | 1026.03
4M | 4642.47 | 4583.8 | 4074.93 | 3557.51 | 3337.59 | 2898.78 | 2535.22 | 2248.83 | 2227.41 | 2203.98 | 2187.29 | 2164.18 | 2156.96 | 2148.52 | 2146.83 | 2131.36 | 2038.29 | 2060.87
2M | 4674.06 | 4659.06 | 4153.1 | 4016.4 | 3540.78 | 3027.05 | 2625.06 | 2321.73 | 2306.4 | 2292.86 | 2282.38 | 2270.35 | 2264.14 | 2259.8 | 2260.46 | 2261.54 | 2224.92 | 2431.58
1M | 4673.77 | 4656.98 | 4156.32 | 4012.65 | 3535.85 | 3021.82 | 2623.08 | 2318.19 | 2303.72 | 2291.55 | 2280.42 | 2270.24 | 2264.82 | 2261.86 | 2261.31 | 2271.41 | 2237.27 | 2432.74
512K | 4673 | 4658.05 | 4267.3 | 4052.55 | 3730.88 | 3236.67 | 2839.93 | 2527.15 | 2513.25 | 2503.12 | 2494.19 | 2517.44 | 2523.1 | 2551.67 | 2555.53 | 2477.41 | 2420.17 | 2590.64
256K | 4672.31 | 4645.58 | 4300.1 | 4091.3 | 3890.2 | 3175.38 | 2748.26 | 2351.27 | 2518.38 | 2627.49 | 2644.71 | 2646.45 | 2690.79 | 2715.46 | 2762.7 | 2445.48 | 2440.11 | 2560.87
128K | 4669.89 | 4661.44 | 4661.75 | 4570.55 | 4453.42 | 4070.1 | 3626.17 | 2349.05 | 3332.47 | 3318.78 | 3328.21 | 3312.1 | 3351.75 | 3197.56 | 3342.59 | 3330.51 | 3335.4 | 3374.9
64K | 4664.69 | 4647.96 | 4646.51 | 4575.1 | 4473.68 | 4218.51 | 3642.61 | 3334.78 | 3395.82 | 3398 | 3403.08 | 3411.87 | 3395.99 | 3299.01 | 4287.45 | 3416.74 | 3389.13 | 3374.16
32K | 4654.62 | 4624.5 | 4631.69 | 4615.62 | 4600.39 | 4585.6 | 4572.8 | 4809.1 | 4803.13 | 4789.7 | 4790.97 | 4784.65 | 4754.23 | 4768.54 | 4750.25 | 4742.01 | 6545.16 | 6408.41
Intel Core i7
32 KB L1 i-cache
32 KB L1 d-cache
256 KB unified L2 cache
8M unified L3 cache
All caches on-chip

## Slide 43: The Memory Mountain
Chart: Stride (x8 bytes)
| s1 | s2 | s3 | s4 | s5 | s6 | s7 | s8 | s9 | s10 | s11 | s12 | s13 | s14 | s15 | s16 | s32 | s64
64M | 4029.59 | 2752.75 | 2159.29 | 1710.75 | 1391.48 | 1176.29 | 1015.77 | 890.72 | 845.57 | 805.46 | 773.78 | 757.94 | 727.91 | 712.66 | 705.63 | 701.98 | 598.19 | 601.22
32M | 4029.36 | 2752.39 | 2160.62 | 1710.98 | 1391.5 | 1176.54 | 1016.71 | 891.8 | 846.98 | 807.22 | 775.18 | 760.41 | 730.74 | 714.98 | 709.26 | 708.88 | 608.99 | 607.39
16M | 4040.1 | 2788.42 | 2188.92 | 1742.97 | 1421.69 | 1201.31 | 1038.37 | 911.7 | 870.39 | 835.31 | 809.25 | 798.05 | 780.28 | 778.37 | 787.2 | 744.13 | 633.53 | 608.86
8M | 4374.01 | 3610.74 | 3002.03 | 2492.39 | 2131.04 | 1821.71 | 1564.14 | 1414.18 | 1404.78 | 1408.59 | 1423.67 | 1456.86 | 1499.61 | 1600.13 | 1667.47 | 1231.7 | 1078.97 | 1026.03
4M | 4642.47 | 4583.8 | 4074.93 | 3557.51 | 3337.59 | 2898.78 | 2535.22 | 2248.83 | 2227.41 | 2203.98 | 2187.29 | 2164.18 | 2156.96 | 2148.52 | 2146.83 | 2131.36 | 2038.29 | 2060.87
2M | 4674.06 | 4659.06 | 4153.1 | 4016.4 | 3540.78 | 3027.05 | 2625.06 | 2321.73 | 2306.4 | 2292.86 | 2282.38 | 2270.35 | 2264.14 | 2259.8 | 2260.46 | 2261.54 | 2224.92 | 2431.58
1M | 4673.77 | 4656.98 | 4156.32 | 4012.65 | 3535.85 | 3021.82 | 2623.08 | 2318.19 | 2303.72 | 2291.55 | 2280.42 | 2270.24 | 2264.82 | 2261.86 | 2261.31 | 2271.41 | 2237.27 | 2432.74
512K | 4673 | 4658.05 | 4267.3 | 4052.55 | 3730.88 | 3236.67 | 2839.93 | 2527.15 | 2513.25 | 2503.12 | 2494.19 | 2517.44 | 2523.1 | 2551.67 | 2555.53 | 2477.41 | 2420.17 | 2590.64
256K | 4672.31 | 4645.58 | 4300.1 | 4091.3 | 3890.2 | 3175.38 | 2748.26 | 2351.27 | 2518.38 | 2627.49 | 2644.71 | 2646.45 | 2690.79 | 2715.46 | 2762.7 | 2445.48 | 2440.11 | 2560.87
128K | 4669.89 | 4661.44 | 4661.75 | 4570.55 | 4453.42 | 4070.1 | 3626.17 | 2349.05 | 3332.47 | 3318.78 | 3328.21 | 3312.1 | 3351.75 | 3197.56 | 3342.59 | 3330.51 | 3335.4 | 3374.9
64K | 4664.69 | 4647.96 | 4646.51 | 4575.1 | 4473.68 | 4218.51 | 3642.61 | 3334.78 | 3395.82 | 3398 | 3403.08 | 3411.87 | 3395.99 | 3299.01 | 4287.45 | 3416.74 | 3389.13 | 3374.16
32K | 4654.62 | 4624.5 | 4631.69 | 4615.62 | 4600.39 | 4585.6 | 4572.8 | 4809.1 | 4803.13 | 4789.7 | 4790.97 | 4784.65 | 4754.23 | 4768.54 | 4750.25 | 4742.01 | 6545.16 | 6408.41
Intel Core i7
32 KB L1 i-cache
32 KB L1 d-cache
256 KB unified L2 cache
8M unified L3 cache
All caches on-chip
Slopes of
spatial
locality

## Slide 44: The Memory Mountain
Chart: Stride (x8 bytes)
| s1 | s2 | s3 | s4 | s5 | s6 | s7 | s8 | s9 | s10 | s11 | s12 | s13 | s14 | s15 | s16 | s32 | s64
64M | 4029.59 | 2752.75 | 2159.29 | 1710.75 | 1391.48 | 1176.29 | 1015.77 | 890.72 | 845.57 | 805.46 | 773.78 | 757.94 | 727.91 | 712.66 | 705.63 | 701.98 | 598.19 | 601.22
32M | 4029.36 | 2752.39 | 2160.62 | 1710.98 | 1391.5 | 1176.54 | 1016.71 | 891.8 | 846.98 | 807.22 | 775.18 | 760.41 | 730.74 | 714.98 | 709.26 | 708.88 | 608.99 | 607.39
16M | 4040.1 | 2788.42 | 2188.92 | 1742.97 | 1421.69 | 1201.31 | 1038.37 | 911.7 | 870.39 | 835.31 | 809.25 | 798.05 | 780.28 | 778.37 | 787.2 | 744.13 | 633.53 | 608.86
8M | 4374.01 | 3610.74 | 3002.03 | 2492.39 | 2131.04 | 1821.71 | 1564.14 | 1414.18 | 1404.78 | 1408.59 | 1423.67 | 1456.86 | 1499.61 | 1600.13 | 1667.47 | 1231.7 | 1078.97 | 1026.03
4M | 4642.47 | 4583.8 | 4074.93 | 3557.51 | 3337.59 | 2898.78 | 2535.22 | 2248.83 | 2227.41 | 2203.98 | 2187.29 | 2164.18 | 2156.96 | 2148.52 | 2146.83 | 2131.36 | 2038.29 | 2060.87
2M | 4674.06 | 4659.06 | 4153.1 | 4016.4 | 3540.78 | 3027.05 | 2625.06 | 2321.73 | 2306.4 | 2292.86 | 2282.38 | 2270.35 | 2264.14 | 2259.8 | 2260.46 | 2261.54 | 2224.92 | 2431.58
1M | 4673.77 | 4656.98 | 4156.32 | 4012.65 | 3535.85 | 3021.82 | 2623.08 | 2318.19 | 2303.72 | 2291.55 | 2280.42 | 2270.24 | 2264.82 | 2261.86 | 2261.31 | 2271.41 | 2237.27 | 2432.74
512K | 4673 | 4658.05 | 4267.3 | 4052.55 | 3730.88 | 3236.67 | 2839.93 | 2527.15 | 2513.25 | 2503.12 | 2494.19 | 2517.44 | 2523.1 | 2551.67 | 2555.53 | 2477.41 | 2420.17 | 2590.64
256K | 4672.31 | 4645.58 | 4300.1 | 4091.3 | 3890.2 | 3175.38 | 2748.26 | 2351.27 | 2518.38 | 2627.49 | 2644.71 | 2646.45 | 2690.79 | 2715.46 | 2762.7 | 2445.48 | 2440.11 | 2560.87
128K | 4669.89 | 4661.44 | 4661.75 | 4570.55 | 4453.42 | 4070.1 | 3626.17 | 2349.05 | 3332.47 | 3318.78 | 3328.21 | 3312.1 | 3351.75 | 3197.56 | 3342.59 | 3330.51 | 3335.4 | 3374.9
64K | 4664.69 | 4647.96 | 4646.51 | 4575.1 | 4473.68 | 4218.51 | 3642.61 | 3334.78 | 3395.82 | 3398 | 3403.08 | 3411.87 | 3395.99 | 3299.01 | 4287.45 | 3416.74 | 3389.13 | 3374.16
32K | 4654.62 | 4624.5 | 4631.69 | 4615.62 | 4600.39 | 4585.6 | 4572.8 | 4809.1 | 4803.13 | 4789.7 | 4790.97 | 4784.65 | 4754.23 | 4768.54 | 4750.25 | 4742.01 | 6545.16 | 6408.41
Intel Core i7
32 KB L1 i-cache
32 KB L1 d-cache
256 KB unified L2 cache
8M unified L3 cache
All caches on-chip
Slopes of
spatial
locality
Ridges of
Temporal
locality

## Slide 45: Today
Cache organization and operation
Performance impact of caches
  The memory mountain
  Rearranging loops to improve spatial locality
  Using blocking to improve temporal locality

## Slide 46: Miss Rate Analysis for Matrix Multiply
Assume:
  Line size = 32B (big enough for four 64-bit words)
  Matrix dimension (N) is very large
    Approximate 1/N as 0.0
  Cache is not even big enough to hold multiple rows
Analysis Method:
  Look at access pattern of inner loop
A
k
i
B
k
j
C
i
j

## Slide 47: Matrix Multiplication Example
Description:
  Multiply N x N matrices
  O(N3) total operations
  N reads per source element
  N values summed per destination
    but may be able to hold in register
/* ijk */
for (i=0; i<n; i++) {
for (j=0; j<n; j++) {
sum = 0.0;
for (k=0; k<n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum;
}
}
Variable sum
held in register

## Slide 48: Layout of C Arrays in Memory (review)
C arrays allocated in row-major order
  each row in contiguous memory locations
Stepping through columns in one row:
  for (i = 0; i < N; i++)
    sum += a[0][i];
  accesses successive elements
  if block size (B) > 4 bytes, exploit spatial locality
    compulsory miss rate = 4 bytes / B
Stepping through rows in one column:
  for (i = 0; i < n; i++)
    sum += a[i][0];
  accesses distant elements
  no spatial locality!
    compulsory miss rate = 1 (i.e. 100%)

## Slide 49: Matrix Multiplication (ijk)
/* ijk */
for (i=0; i<n; i++) {
for (j=0; j<n; j++) {
sum = 0.0;
for (k=0; k<n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum;
}
}
A
B
C
(i,*)
(*,j)
(i,j)
Inner loop:
Column-
wise
Row-wise
Fixed
Misses per inner loop iteration:
  A B C
  0.25 1.0 0.0

## Slide 50: Matrix Multiplication (jik)
/* jik */
for (j=0; j<n; j++) {
for (i=0; i<n; i++) {
sum = 0.0;
for (k=0; k<n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum
}
}
A
B
C
(i,*)
(*,j)
(i,j)
Inner loop:
Row-wise
Column-
wise
Fixed
Misses per inner loop iteration:
  A B C
  0.25 1.0 0.0

## Slide 51: Matrix Multiplication (kij)
/* kij */
for (k=0; k<n; k++) {
for (i=0; i<n; i++) {
r = a[i][k];
for (j=0; j<n; j++)
c[i][j] += r * b[k][j];
}
}
A
B
C
(i,*)
(i,k)
(k,*)
Inner loop:
Row-wise
Row-wise
Fixed
Misses per inner loop iteration:
  A B C
  0.0 0.25 0.25

## Slide 52: Matrix Multiplication (ikj)
/* ikj */
for (i=0; i<n; i++) {
for (k=0; k<n; k++) {
r = a[i][k];
for (j=0; j<n; j++)
c[i][j] += r * b[k][j];
}
}
A
B
C
(i,*)
(i,k)
(k,*)
Inner loop:
Row-wise
Row-wise
Fixed
Misses per inner loop iteration:
  A B C
  0.0 0.25 0.25

## Slide 53: Matrix Multiplication (jki)
/* jki */
for (j=0; j<n; j++) {
for (k=0; k<n; k++) {
r = b[k][j];
for (i=0; i<n; i++)
c[i][j] += a[i][k] * r;
}
}
A
B
C
(*,j)
(k,j)
Inner loop:
(*,k)
Column-
wise
Column-
wise
Fixed
Misses per inner loop iteration:
  A B C
  1.0 0.0 1.0

## Slide 54: Matrix Multiplication (kji)
/* kji */
for (k=0; k<n; k++) {
for (j=0; j<n; j++) {
r = b[k][j];
for (i=0; i<n; i++)
c[i][j] += a[i][k] * r;
}
}
A
B
C
(*,j)
(k,j)
Inner loop:
(*,k)
Fixed
Column-
wise
Column-
wise
Misses per inner loop iteration:
  A B C
  1.0 0.0 1.0

## Slide 55: Summary of Matrix Multiplication
ijk (& jik):
  2 loads, 0 stores
  misses/iter = 1.25
kij (& ikj):
  2 loads, 1 store
  misses/iter = 0.5
jki (& kji):
  2 loads, 1 store
  misses/iter = 2.0
for (i=0; i<n; i++) {
for (j=0; j<n; j++) {
sum = 0.0;
for (k=0; k<n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum;
}
}
for (k=0; k<n; k++) {
for (i=0; i<n; i++) {
r = a[i][k];
for (j=0; j<n; j++)
c[i][j] += r * b[k][j];
}
}
for (j=0; j<n; j++) {
for (k=0; k<n; k++) {
r = b[k][j];
for (i=0; i<n; i++)
c[i][j] += a[i][k] * r;
}
}

## Slide 56: Core i7 Matrix Multiply Performance
Chart: Array size (n)
| 50.0 | 100.0 | 150.0 | 200.0 | 250.0 | 300.0 | 350.0 | 400.0 | 450.0 | 500.0 | 550.0 | 600.0 | 650.0 | 700.0 | 750.0
jki | 6.4 | 6.87 | 4.14 | 5.53 | 10.93 | 33.23 | 49.43 | 51.49 | 52.06 | 52.06 | 52.07 | 52.09 | 52.12 | 52.17 | 52.2
kji | 6.4 | 6.82 | 4.01 | 5.33 | 11.04 | 33.21 | 49.42 | 51.5 | 52.07 | 52.08 | 52.09 | 52.1 | 52.14 | 52.19 | 52.23
ijk | 5.31 | 6.35 | 6.29 | 3.7 | 3.72 | 3.71 | 3.72 | 3.83 | 4.6 | 7.74 | 11.71 | 16.54 | 20.57 | 23.85 | 23.86
jik | 5.4 | 6.23 | 3.64 | 3.71 | 3.61 | 3.6 | 3.63 | 3.74 | 4.64 | 7.57 | 11.62 | 16.44 | 20.44 | 23.68 | 23.66
kij | 4.37 | 5.36 | 3.23 | 3.32 | 3.29 | 3.24 | 3.2 | 3.17 | 3.16 | 3.14 | 3.13 | 3.12 | 3.1 | 3.1 | 3.08
ikj | 3.58 | 5.31 | 3.19 | 3.18 | 3.15 | 3.12 | 3.1 | 3.1 | 3.11 | 3.09 | 3.07 | 3.06 | 3.02 | 3.02 | 3.01
jki / kji
ijk / jik
kij / ikj

## Slide 57: Today
Cache organization and operation
Performance impact of caches
  The memory mountain
  Rearranging loops to improve spatial locality
  Using blocking to improve temporal locality

## Slide 58: Example: Matrix Multiplication
a
b
i
j
*
c
=
c = (double *) calloc(sizeof(double), n*n);
/* Multiply n x n matrices a and b */
void mmm(double *a, double *b, double *c, int n) {
int i, j, k;
for (i = 0; i < n; i++)
for (j = 0; j < n; j++)
for (k = 0; k < n; k++)
c[i*n+j] += a[i*n + k]*b[k*n + j];
}

## Slide 59: Cache Miss Analysis
Assume:
  Matrix elements are doubles
  Cache block = 8 doubles
  Cache size C << n (much smaller than n)
First iteration:
  n/8 + n = 9n/8 misses
  Afterwards in cache: (schematic)
*
=
n
*
=
8 wide

## Slide 60: Cache Miss Analysis
Assume:
  Matrix elements are doubles
  Cache block = 8 doubles
  Cache size C << n (much smaller than n)
Second iteration:
  Again: n/8 + n = 9n/8 misses
Total misses:
  9n/8 * n2 = (9/8) * n3
n
*
=
8 wide

## Slide 61: Blocked Matrix Multiplication
c = (double *) calloc(sizeof(double), n*n);
/* Multiply n x n matrices a and b */
void mmm(double *a, double *b, double *c, int n) {
int i, j, k;
for (i = 0; i < n; i+=B)
for (j = 0; j < n; j+=B)
for (k = 0; k < n; k+=B)
/* B x B mini matrix multiplications */
for (i1 = i; i1 < i+B; i++)
for (j1 = j; j1 < j+B; j++)
for (k1 = k; k1 < k+B; k++)
c[i1*n+j1] += a[i1*n + k1]*b[k1*n + j1];
}
a
b
i1
j1
*
c
=
c
+
Block size B x B

## Slide 62: Cache Miss Analysis
Assume:
  Cache block = 8 doubles
  Cache size C << n (much smaller than n)
  Three blocks fit into cache: 3B2 < C
First (block) iteration:
  B2/8 misses for each block
  2n/B * B2/8 = nB/4 (omitting matrix c)
  Afterwards in cache (schematic)
*
=
*
=
Block size B x B
n/B blocks

## Slide 63: Cache Miss Analysis
Assume:
  Cache block = 8 doubles
  Cache size C << n (much smaller than n)
  Three blocks fit into cache: 3B2 < C
Second (block) iteration:
  Same as first iteration
  2n/B * B2/8 = nB/4
Total misses:
  nB/4 * (n/B)2 = n3/(4B)
*
=
Block size B x B
n/B blocks

## Slide 64: Summary
No blocking: (9/8) * n3
Blocking: 1/(4B) * n3
Suggest largest possible block size B, but limit 3B2 < C!
Reason for dramatic difference:
  Matrix multiplication has inherent temporal locality:
    Input data: 3n2, computation 2n3
    Every array elements used O(n) times!
  But program has to be written properly

## Slide 65: Concluding Observations
Programmer can optimize for cache performance
  How data structures are organized
  How data are accessed
    Nested loop structure
    Blocking is a general technique
All systems favor “cache friendly code”
  Getting absolute optimum performance is very platform specific
    Cache sizes, line sizes, associativities, etc.
  Can get most of the advantage with generic code
    Keep working set reasonably small (temporal locality)
    Use small strides (spatial locality)